## Slide 1: An Elegant Solution for Safe Water on Tap
Monroe Weber-Shirk

## Slide 2: Three ideas…
Evolution – Iteration – Mistakes - Learning
Creativity for Environmental Engineers can be expressed in how we solve the challenges of the interaction between fluids, particles, and geometry
It’s about details! (It is about all of the things that traditional textbooks tend to ignore.)
  Density currents caused by temperature change
  Flow distribution to reduce mean currents

## Slide 3: Inventing Perfection
“Furthermore, as the full scale plant is already in operation, the need for further design changes is not clear.” -(Anonymous Reviewer)
Ideas spring fully formed from their creator’s mind?
Athena leaped from Zeus's head, fully grown and armed
http://designserver.cee.cornell.edu/Designs
Notes: What about iteration and feedback?

## Slide 4: AguaClara Consortium
Finance
Implement
R&D
Transfer
Operate
Market
Municipalities
Municipalities
Water Boards
Implementers

## Slide 5
donors
Finance Research/Invent/Design/Engage
Consulting firms
graduates
Cornell connections
Cornell Institute for Public Affairs
Architecture Art Planning
Atkinson Center
Tata-Cornell Institute

## Slide 6
Water Board
Design tool
AguaClara Engineers
Implementation Partners
Finance Implementation
Municipalities

## Slide 7
Water Board
Design tool
donors
Finance Research/Invent/Design/Engage
AguaClara Engineers
Finance Implementation
Consulting firms
Implementation Partners
graduates
AguaClara Consortium
Municipalities
Cornell connections
Cornell Institute for Public Affairs
Architecture Art Planning
Atkinson Center
Tata-Cornell Institute

## Slide 8: What is the conventional high tech solution?
Technologies from the early 1900’s: flocculation – sedimentation – filtration – disinfection
“Advances” over the last 50 years have focused on automation and increased use of electricity
Increased cost, reduced reliability, more difficult to maintain, reduced useful life (cell phone life)
50% of the high tech plants that were installed in Honduras since 2003 have been abandoned

## Slide 9: What happens when high tech water meets small town?
Software expires and no one is able or willing to pay for the upgrade
Everything that moves fails!
  Valves, pumps, compressors, switches, relays
Electricity bill is too high
Entire treatment plant is abandoned
3 year average life for package plants installed in Africa – World Bank Engineer

## Slide 10: Simple, Elegant, or Complicated?
“Any intelligent fool can make things bigger, more complex, and more violent. It takes a touch of genius — and a lot of courage – to move in the opposite direction.” --- E.F. Schumacher
“Simplicity is the ultimate sophistication.” --- Leonardo da Vinci

## Slide 11: Elegant Solution
Solves the problem very well
No unnecessary complexity
Easy to understand
Simple and beautiful
  Bicycle
  Windmills
Context matters in defining elegant!

## Slide 12: Pride of Ownership
What happens when the check engine light goes on in your car?
What do you do if your bicycle brakes need to be adjusted?
What does the plant operator do if the chemical feed stops working?
We want the plant operator to diagnose and fix the problem without needing to call anyone.

## Slide 13: AguaClara Technologies
Chemical dosing
Rapid Mix
Flocculator
Sedimentation
Filtration
Conclusions

## Slide 14: Stages of particle removal
Filtration
Sedimentation
Flocculation
Coagulation
Nanoglob deposition
Collisions
Gravity!
Floc Blanket
More Collisions
Last chance!
Notes: Here are the five stages of colloid or particle removal in hydraulic drinking water treatment plants. The first stage, coagulation, involves the addition of a chemical coagulant to destabilize a suspension of particles. The coagulant precipitates and attaches to the particle surface. Then in flocculation, velocity gradients in the water cause the particles (now coated in precipitated coagulant) to collide and stick to one another forming aggregates. In floc blankets there are many more opportunities for collisions. In sedimentation, fluid flow is very slow and the aggregates settle to the bottom of the tank. Filtration is often used to remove any remaining particles but is not included in the bench-scale setup.

## Slide 15
Flocculator
Chemical Stock Tanks
Chemical Dosing
Entrance Tank
Sedimentation
Open Stacked Rapid Sand (OStaRS) Filter
Drain Channel

## Slide 16: Tour of an AguaClara plant

## Slide 17
Elevated flocculator
Entrance Tank
Sedimentation Tank

## Slide 19
What do you see?
Why did this happen?

## Slide 22: Flocculator Channels

## Slide 24: What do you see?

## Slide 25: What is the difference between laser level and water level?
Suppose I am building a really big structure…

## Slide 36
Double bay sedimentation tank design. No longer recommended!

## Slide 38
Sed tank drains!

## Slide 47
Flocculated Water Entering the Sedimentation Tank
Settled Water

## Slide 48: Three Key Innovations
AguaClara is open source engineering:
  Many inventions, ZERO patents
  Our technologies are described on our website and published in the literature.
  Our example designs are available on the web!
  Our technologies use ZERO electricity (except for batteries in the turbidimeters)
Some plant performance data is online

## Slide 49: How Much Does it Cost?
CAPITAL COST
$50,000 + $8000 per L/s of capacity*
OPERATING COST
$5 per person per year
or $50 per million liters
ELECTRICITY COST
ZERO
Notes: Quick and rough cost estimates.

## Slide 50: Reflections
Technology and Engineering Philosophy matter!
Infrastructure failures often have multiple causes and many of them are linked to design choices
We design for Simplicity on the other side of Complexity