## Slide 1: Drinking Water Contaminants

## Slide 2: Class announcements
Python Tutorial 1 due on Tuesday night
Read entire tutorial up to and including problem 10 before starting to code
PLAY: Write some simple code (perhaps rewrite the PV=nRT problem – solve for a different variable)
Why did we create functions (aide_design)?
Head loss (major and minor)
This is not a Python Class – functions, units, graphs, print
Notes: Use tools!

## Slide 3: Water Quality
History of our understanding of waterborne disease
Brief history of water treatment
Drinking Water Standards: how do we decide what is allowed in the water we drink?

## Slide 4: The flush toilet contaminates safe drinking water with feces
Toilets made cities habitable by carrying human waste “away”
Unfortunately “away” was too close…
  In the early 1800s new flush toilets and sewers carried the waste directly into rivers and streams
  Chicago!
  London drained its raw sewage into and withdrew its drinking water from the Thames River, both without any treatment.
  Several of the drinking water intakes were below sewage outfalls!

## Slide 5: Chicago Sanitary and Ship Canal 1892: a creative solution

## Slide 6: Southwark and Vauxhall Water Company
In 1850, the microbiologist Arthur Hassall wrote of the River Thames water they were using,"...a portion of the inhabitants of the metropolis are made to consume, in some form or another, a portion of their own excrement, and moreover, to pay for the privilege."
Next Cartoon presents John Edwards, owner of the Southwark Water Company, posing as Neptune ("Sovereign of the Scented Streams"). He is seen crowned with a chamber-pot, seated on a stool on top of a cesspool which doubles as the water-intake for the Southwark Water Company customers in south London.
Notes: http://www.ph.ucla.edu/epi/snow/southwarkwatercompany.html (comments)

## Slide 7: Southwark and Vauxhall Water Company
Courtesy of the National Library of Medicine
Notes: http://wwwihm.nlm.nih.gov/ihm/images/A/24/183.jpg
Direct reuse without treatment

## Slide 8: Drinking Water Treatment and Germ Theory
1829: First sand filter used to treat some of London's drinking water
1850: John Snow established the link between drinking water (from a contaminated well) and Cholera
1872: Poughkeepsie, NY installs first filter in US
1885: Sand filters are shown to remove bacteria
1892: Cholera outbreak in Hamburg, Germany

## Slide 9: 1892 Cholera outbreak in Hamburg Germany
Large outbreak of Cholera in Hamburg
17,000 cases; 8,600 deaths
Very few cases in neighborhoods served by Altona's filtered water supply
Hamburg's sewers were upstream from Altona's intake!
Altona's water intake and filter beds
Hamburg's sewer outfalls
Hamburg
Altona
Elbe River
Hamburg's water intake

## Slide 10: Altona vs. Hamburg: Cholera Cases
Hamburg
Altona
Cases in Altona acquired in Hamburg
Cholera cases
Received water from Altona
Cholera was waterborne
Slow sand filtration may have protected Altona
Conclusions

## Slide 11: Lake Titicaca in the Andes Mountains
Notes: We’d like to know what the status of the sewer system is on the island
If people are currently using latrines and then switch to toilets when they have more water, then we could have an unintended side effect of more untreated wastewater going into the lake. And the lake is their best source of water.

## Slide 12: Fecal-Oral Pathways: a stochastic process
Human excreta
Animal excreta
Dry sanitation involving reuse
Waterborne sewage
Non recycling latrines
Soil
Surface water
Ground water
Food
Drinking water
Oral
Pathogen source
Sanitation method
Land application
Environment
Transport
Hands
Crops
Flies
Water
Hygiene
Water treatment
Sanitation
washing
Will you see an immediate improvement in public health with the installation of a water treatment plant?
Notes: What technology that is commonly found in homes plays an important role in breaking the Fecal-Oral pathway? SINKS!

## Slide 13
Notes: What are two fecal oral pathways?
How will cap be removed?
Where does the mouth go?
Wet hand contaminated with dirty water removes cap
Hands carry feces if handwashing is not easy.

## Slide 14: Waterborne Threats to Human Health
Infectious diseases
  caused by viruses, bacteria, protozoa (pathogens)
  https://confluence.cornell.edu/display/cee4540/Bad+Bugs
Noninfectious diseases
  _____: caused by short term exposure to harmful chemicals
  _______: caused by long term exposure to harmful chemicals
    low levels of exposure to certain chemicals over a long period of time may cause cancer, liver and kidney damage, or central nervous system damage
acute
chronic

## Slide 15: Propose a Drinking Water Standard
You have been granted the authority to regulate drinking water quality. Create a standard for the concentrations of disease-causing organisms in drinking water.
In the absence of technological/economic constraints,
  Which pathogens would you regulate?
  What concentration would you choose?
Given technological and economic constraints how might you change your regulation?
Setting the standards

## Slide 16: Optimal Pathogen Exposure
Should we be exposed to small doses of pathogens so we build up our resistance?
How could we build pathogen exposure into our daily lives?
Potential application
  Common cold (continues to mutate)
  Norwalk virus (Immunity, however, is not permanent and re-infection can occur after 2 years)
  HIV (no immunity)
  The case of Typhoid
Early exposure to germs has lasting benefits. Nature, March 2012
Immune systems of healthy adults 'remember' germs to which they’ve never been exposed, Stanford study Feb 2013
Notes: Do you ask friends to cough on you?

## Slide 17: Safe Drinking Water Act (1974)
mandatory
suggested
Specific standards for drinking water
  primary (__________)
  secondary (__________ upper limits for non-health related parameters)
Applicable to all water supplies serving more than 25 people or having 15 or more service connections
Enforced by U.S. Environmental Protection Agency

## Slide 18: Primary Standards: (Health) 6 Broad Categories
Microorganisms
Disinfectants
Disinfection Byproducts
Inorganic Chemicals
Organic Chemicals
Radionuclides
Where is “dirt”?

## Slide 19: Primary Standards: (Health) Inorganic chemicals (units of mg/L)
Contaminant U.S. EPA
Antimony 0.006
Arsenic 0.01
Asbestos (fiber >10 micrometers) 7 MFL
Barium 2
Beryllium 0.004
Cadmium 0.005
Chromium (total) 0.1
Copper Action Level=1.3; TT8
Cyanide (as free cyanide) 0.2
Fluoride 4.0
Lead Action Level=0.015; TT8
Inorganic Mercury 0.002
Nitrate (measured as Nitrogen) 10
Nitrite (measured as Nitrogen) 1
Selenium 0.05
Thallium 0.002
Notes: http://water.epa.gov/drink/contaminants/index.cfm
Also see WHO at http://www.who.int/water_sanitation_health/dwq/2edvol1c.pdf?ua=1

## Slide 20: Primary Standards: (Health) A Few Organic Chemicals (units of mg/L) see the complete list!
Contaminant MCLG MCL
Acrylamide zero TT7
Alachlor zero 0.002
Atrazine 0.003 0.003
Benzene zero 0.005
1-1-Dichloroethylene 0.007 0.007
Dioxin (2,3,7,8-TCDD) zero 0.00000003
Epichlorohydrin zero TT7
Ethylbenzene 0.7 0.7
Ethelyne dibromide zero 0.00005
Lindane 0.0002 0.0002
Polychlorinated biphenyls (PCBs) zero 0.0005
Tetrachloroethylene zero 0.005
Toluene 1 1
Total Trihalomethanes (TTHMs) none5 0.10
Trichloroethylene zero 0.005
Vinyl chloride zero 0.002
Xylenes (total) 10 10

## Slide 21: Primary Standards : (Health) Related to Microorganisms
Contaminant MCLG MCL
Cryptosporidium zero TT3
Giardia lamblia zero TT3
Legionella zero TT3
Viruses (enteric) zero TT3
Heterotrophic plate count N/A TT3
Total Coliforms zero 5.0%4
Turbidity N/A TT3
Cause disease
Indicators
Pathogens are a subset of particles

## Slide 22: Microbial Contaminants
For microbial contaminants that may present public health risk, the MCLG is set at zero because ingesting one protozoa, virus, or bacterium may cause adverse health effects.
The MCL is set as close to the MCLG as feasible, (the level that may be achieved with the use of the best available technology, treatment techniques, and other means which EPA finds are available), taking cost into consideration.

## Slide 23: Treatment Technique (TT)
When there isn’t an economical and technically feasible method to measure a contaminant, a Treatment Technique is set rather than an MCL.
A treatment technique is an enforceable procedure or level of technological performance which public water systems must follow to ensure control of a contaminant.
  Surface Water Treatment Rule (disinfection and filtration)
  Lead and Copper Rule (optimized corrosion control).

## Slide 24: Turbidity
A measure of the scattering of light by particles in a suspension
A turbid water sample appears cloudy or “dirty”
High turbidity is the result of lots of light scattering caused by the particles in suspension
Measured in NTU (Nephelometric Turbidity Units)
cloud

## Slide 25: Turbidity Measurements
90° detector
lamp
lens
sample cell
180° detector
LED
sample cell
170° detector
Turbidity Sensors (approximate turbidity measurement)

## Slide 26: Secondary Standards: Aesthetics
Contaminant U.S. EPA, 1993 WHO, 1984
Aluminum 0.5-0.2 mg/L 0.2 mg/L
Chloride 250 mg/L 250 mg/L
Color 15 color units 15 color units
Copper 1.0 mg/L 1.0 mg/L
Corrosivity Noncorrosive
Fluoride 2.0 mg/L
Foaming agents 0.5 mg/L
Iron 0.3 mg/L 0.3 mg/L
Manganese 0.05 mg/L 0.1 mg/L
Odor (Threshold Odor Number) 3 TON
pH 6.5-8.5 6.5-8.5
Silver 0.1 mg/L
Sulfate 250 mg/L 400 mg/L
Total dissolved solids 500 mg/L 1000 mg/L
Zinc 5.0 mg/L 5.0 mg/L
Notes: http://water.epa.gov/drink/contaminants/index.cfm#Secondary

## Slide 27: What would you measure before drinking the water?
Surface water (big concern is pathogens)
  Turbidity (pathogens are particles)
  Chlorine residual
Ground water (big concern is still pathogens)
  Turbidity
  Chlorine residual
  Arsenic and fluoride (depending on location)
  Organic chemicals (agricultural and industrial)

## Slide 28: Effect of Chlorination on Inactivating Selected Bacteria
Bacteria | Cl2 (mg/l) | Time (min) | Ct Factor (mg-min/l) | Reduction(%) | Ct for pC* of1 | Reference
Campylobacter jejuni | 0.1 | 5 | 0.5 | 99.99 | 0.125 | Blaser et al, 1986
Escherichia coli | 0.2 | 3 | 0.6 | 99.99 | 0.15 | Ram and Malley, 1984
Legionella pneumophila | 0.25 | 60-90 | 18.75 | 99 | 9.4 | Kuchta et al, 1985
Mycobacterium chelonei | 0.7 | 60 | 42 | 99.95 | 13 | Carson et al, 1978
Mycobacterium fortuitum | 1.0 | 30 | 30 | 99.4 | 13.5 | Pelletier and DuMoulin, 1987
Mycobacterium intracellulare | 0.15 | 60 | 9 | 70 | 17.2 | Pelletier and DuMoulin, 1987
Pasteurella tularensis | 0.5-1.0 | 5 | 3.75 | 99.6-100 | 1.6 | Baumann and Ludwig, 1962
Salmonella typhi | 0.5 | 6 | 3 | 99 | 1.5 | Korol et al, 1995
Shigella dysenteriae | 0.05 | 10 | 0.5 | 99.6-100 | 0.2 | Baumann and Ludwig, 1962
Staphylococcus aureus | 0.8 | 0.5 | 0.4 | 100 | -- | Bolton et al, 1988
Vibrio cholerae(smooth strain) | 1.0 | < 1 | < 1 | 100 | -- | Rice et al, 1993
Vibrio cholerae (rugose strain) | 2.0 | 30 | 60 | 99.999 | 12 | Rice et al, 1993
Yersinia enterocolitica | 1.0 | 30 | 30 | 92 | 27 | Paz et al, 1993
Notes: http://www.cdc.gov/safewater/about_pages/chlorinationtable.htm
I calculated the Ct for a pC* of 1. This assumes that chick’s law applies and that die off is proportional to the concentration.

## Slide 29: Effect of Chlorination on Inactivating Selected Viruses
Viruses | Cl2 (mg/l) | Time (min) | Ct factor (mg-min/l) | Reduction (%) | Ct for pC* of1 | Reference
Adenovirus | 0.2 | 40-50 sec | 0.15 | 99.8 | 0.06 | Clarke et al, 1956
Coxsackie | 0.16-0.18 | 3.8 | 0.06 | 99.6 | 0.025 | Clarke and Kabler, 1954
Hepatitis A | 0.42 | 1 | 0.42 | 99.99 | 0.105 | Grabow et al, 1983
Norwalk | 0.5-1.0 | 30 | 22.5 | -- | -- | Keswick et al, 1985
Parvovirus | 0.2 | 3.2 | 0.64 | 99 | 0.32 | Churn et al, 1984
Poliovirus | 0.5-1.0 | 30 | 22.5 | 100 | -- | Keswick et al, 1985
Rotavirus | 0.5-1.0 | 30 | 22.5 | 100 | -- | Keswick et al, 1985
Notes: http://www.cdc.gov/safewater/about_pages/chlorinationtable.htm
I calculated the Ct for a pC* of 1. This assumes that chick’s law applies and that die off is proportional to the concentration.

## Slide 30: Effect of Chlorination on Inactivating Selected Protozoa
Protozoa | Cl2 (mg/l) | Time (min) | Ct Factor (mg-min/l) | Reduction (%) | Ct for pC* of 1 | Reference
Cryptosporidium parvum | 80 | 90 | 7200* | 90 | 7200 | Korich et al, 1990
Entamoeba histolytica | 1.0 | 50 | 50 | 100 | -- | Snow, 1956
Giardia lamblia | -- | -- | 68-389 | 99.9 | 30 | AWWA, 1999
Naegleria fowleri | 0.5-1.0 | 60 | 45 | 99.99 | 11 | de Jonckheere and van de Voorde, 1976
How many pathogens does it take to make you sick?
https://confluence.cornell.edu/display/cee4540/Bad+Bugs
Notes: http://www.cdc.gov/safewater/about_pages/chlorinationtable.htm
I calculated the Ct for a pC* of 1. This assumes that chick’s law applies and that die off is proportional to the concentration.

## Slide 31: Which pathogens are a big concern even with Chlorine?
Pathogens with a small infective dose and high resistance to chlorine
  Cryptosporidium parvum
  Giardia lamblia

## Slide 32: Summary
The causes of many waterborne disease have been identified
Standards for microbiological and chemical contaminants have been set by US EPA and the World Health Organization
Waterborne disease continues to be a significant public health concern especially for the poorest 2 billion
Toilets (pollute the environment) and Sinks (clean our hands)