## Slide 1: The State of the Planet
Sustainable Development Goals

## Slide 2: Class Logistics
Field trip date
Course notes – recommend printing PDF starting with Flow Control and Measurement

## Slide 3: Outline
Burden of unsafe water
The Sustainable Development Goals
  Safe and Improved…
Intermittent Supplies
The technology is well developed…
  Cell phones vs. municipal water technology
A role for universities

## Slide 4: WHO Fact sheet on water (2017): The good news
“In 2015, 71% of the global population (5.2 billion people) used a safely managed drinking-water service – located on premises, available when needed, and free from contamination.”
But let’s bring skepticism to this statement
This conclusion was made without collecting data on water quality in rural areas
(World Health Organization)
Notes: http://www.who.int/mediacentre/factsheets/fs391/en/
https://www.ircwash.org/blog/third-glass-three-quarters-full?utm_source=Amplify&utm_campaign=5c4000cc1e-Amplify_Aug_2017&utm_medium=email&utm_term=0_d60e6862b4-5c4000cc1e-48437621

## Slide 5: UN Fact sheet on water (2017) The bad news
884 million people lack even a basic drinking-water service, including 159 million people who are dependent on surface water
Globally, at least 2 billion people use a drinking water source contaminated with feces
Contaminated water can transmit diseases such diarrhea, cholera, dysentery, typhoid, and polio
Contaminated drinking water is estimated to cause 502 000 diarrheal deaths each year
Notes: http://www.who.int/mediacentre/factsheets/fs391/en/

## Slide 6: UN Fact sheet on water (2015)
By 2025, half of the world’s population will be living in water-stressed areas
In low- and middle-income countries, 38% of health care facilities lack any water source, 19% do not have improved sanitation and 35% lack water and soap for handwashing
Notes: http://www.who.int/mediacentre/factsheets/fs391/en/

## Slide 7: Safe Tap Water According to the CDC
A Traveler's Guide to Tap Water
September 10, 2014 by Danny Ashton
Notes: A Traveler's Guide to Tap Water
September 10, 2014 by Danny Ashton
http://lifehacker.com/know-what-countries-guarantee-drinkable-tap-water-with-1635070463

## Slide 8: Honduras Stats as of 2015 (from WHO)
Population with sustainable access to an improved water source
  Urban – 97.4%
  Rural – 83.8%
Notes: http://apps.who.int/gho/data/node.main.46?lang=en

## Slide 9: More Honduras Stats
In 2006, only 75% of the drinking water in urban areas was disinfected[2] and 10% of the wastewater that was collected received treatment.[3]
In rural areas, it was estimated that only one-third of the systems provided continual service and less than 14% of the systems delivered disinfected water in 2004 .[4]
http://en.wikipedia.org/wiki/Water_supply_and_sanitation_in_Honduras
extra

## Slide 10: Value of Service and Willingness to Pay
Cost of service ($/month)
Willingness to Pay ($/month)
Economics background: cost/quality framework
  How do we understand the failure of some systems?
  Where is the “sweet spot” for sustainability?
Untreated river water at the tap
Traditional Mechanized plant
AguaClara plant
Service method
Break-even line
Minimum quality for public health
2
1
3
Notes: The cases of 1 (small towns less than 25,000) and 2 (towns larger than 25,000) in Honduras are the norm.

## Slide 11: Reina Amador Diaz: Tamara, Honduras
“I used to boil the water for hours and it would still be dirty.” As a cook, Dona Reina saves times by receiving clean water directly into her home. She used to worry about spreading illnesses when she cooked. “Now the water is pure; I know I am serving people healthy, clean food.”
Dona Reina says that the water treatment plant has attracted new residents. “We have cleaner water than the capital!”
extra

## Slide 12: Intermittent Supplies
It is estimated that over one-third of the urban water supplies in Africa, and in Latin America and the Caribbean, and more than half those in Asia, operate intermittently.
Why are supplies intermittent? _______________
  Crude form of rationing
  Lack of meters
  Leaking system – reduce amount of water lost
  Some sections of the city might never receive water otherwise
  Elevation challenges!
Rolling blackouts
Notes: http://www.who.int/docstore/water_sanitation_health/Globassessment/Global3.4.htm

## Slide 13: You just acquired a hotel in downtown Delhi, India
Electricity is intermittent, what do you do?
Water is intermittent, what do you do?
  How can you get more water?
  How does each affect your water quality?

## Slide 14: Leaks don’t cause contamination unless the flow is INTO the pipe
Necessary conditions:
  Saturated contaminated soil
  Leaky Pipe
  Pressure outside pipe must exceed pressure inside pipe
Potential Causes:
  Negative pressure transients
  Booster pumps
*Photo credits
Top: http://texas-slab-leak-repair.com/water_leak
Bottom: Emily Kumple
Notes: David Gold, Alicia Peters, Weier Chen,Lucia Garcia-Iturri Gallego, Distribution System Contamination Prevention
https://docs.google.com/presentation/d/1FbHpETKLk-6JZaqnlvxxkkQqu3iSUCvia9jvmYfr5kg/edit#slide=id.p21

## Slide 15: Booster pumps that pull water from the distribution system should be banned
Image credits: http://www.egr.msu.edu/~fultras-web/images/applications/gui/PressureWaveform.png
Emily Kumple
Pressure Transients
Boster Pumps
Notes: David Gold, Alicia Peters, Weier Chen,Lucia Garcia-Iturri Gallego, Distribution System Contamination Prevention
https://docs.google.com/presentation/d/1FbHpETKLk-6JZaqnlvxxkkQqu3iSUCvia9jvmYfr5kg/edit#slide=id.p16

## Slide 16: Consequences of Intermittent Supplies
Intermittent water supply is a significant constraint on the availability of water for hygiene
  And personal hygiene is very important!!!
Encourages the low-income urban population to turn to alternatives such as water vendors
  That are expensive and from dubious sources
Point of Use Storage
  That may create risk of contamination
Risks of distribution system contamination
extra
Notes: http://www.who.int/docstore/water_sanitation_health/Globassessment/Global3.4.htm

## Slide 17: Consequences of Intermittent Supplies
Contamination may also occur by intrusion of contaminated water into the pipelines through faulty joints, cracks, etc.
Opportunity for contamination by siphoning
Loss of chlorine residual in stagnant water
The pipelines are subject to additional stress caused by transient flows (water hammer), affecting the durability of the system and weakening pipes and joints (more leaks…)
Water waste increases
Complaints about metering air (if there are meters)
extra

## Slide 18: Point of Use (or distributed) Storage
When there is frequent intermittence in the water distribution system, the consumers commonly build or buy domestic storage tanks
Although these devices help to reduce hourly peaks in demand and mask short-term interruptions for users, they are often neither properly protected nor regularly cleaned and disinfected
But they might be a very good idea!
extra
Notes: http://www.who.int/docstore/water_sanitation_health/Globassessment/Global3.4.htm

## Slide 19: Water Storage Tanks
Photo by Chris Boone
extra

## Slide 20: Eliminating Intermittency
Reduce demand – metering
  Meters are expensive or (cheaper and unreliable)
Eliminate leaks
Reducing intermittency is a significant engineering and societal challenge
We need engineers and social scientists to work together and come up with techniques to improve distribution system performance when the water supply is limited
Community size may influence the solution
extra

## Slide 21: The Point of Use (POU) Treatment Option
A Hypothesis – Given that
  centralized water supply systems always have leaks
  intermittency is common when water is in short supply
  contaminated water can flow into the supply pipes when they aren’t pressurized
  Centralized systems often fail to meet standards
Household level (Point of Use) is the best option for drinking water treatment
extra
Notes: Discuss and then vote

## Slide 22: Technology isn’t the problem
Former World Health Organization Director-General: Dr Gro Harlem Brundtland speech at Cornell University in 2005
Loosely paraphrasing…
We have the technology to solve the world’s problems – what is missing is education, institutional capacity, and political will
Notes: This is the “engineers are irrelevant hypothesis”.

## Slide 23
AND
Policy, Education, Institutions
Technologies

## Slide 24: Policy, Education, Institutions or Engineering
You can sometimes compensate for poor engineering by providing more inputs
  Energy – fossil fuels
  Education
  Money
  Management
  Labor
You can sometimes reduce this burden on society by improving the technologies
These factors are multipliers!!!!
and

## Slide 25: Multipliers
1x1x1x1x1x0=0
  Energy x Education x Money x Governance x Labor x Technology = ?
1x1x½x1x1x2=1

## Slide 26: Suppose distillation were the only method that environmental engineers had developed to create clean water
All water in pipes delivered to homes was unsafe
What would you say is the limiting factor preventing implementation of safe piped water?
  Weak institutions
  Corruption
  Weak Economies
  Poor education
  Inadequate technology
What do you conclude?
Notes: We have the technology. The problem is weak economies.

## Slide 27: Why aren’t there better technology choices?
We have a solution that works for strong economies (conventional water treatment)
Individual cities can’t afford to hire consulting firms to conduct research to develop better technologies
Each city chooses conservative existing designs
The same is true for countries in the Global South (they can’t afford the R&D to develop better technologies)
extra

## Slide 28: Continual optimization? Cell Phones vs. Water Treatment
Why are cell phones continually getting cheaper and better?
Why is conventional water treatment not enjoying a similar optimization?
  Vendors, Consultants, Municipalities
  What does each entity strive to obtain?

## Slide 29: Cell Phones vs. Municipal Water Treatment
Global! | Cell phones | Municipal Water
Units per year | 850,000,000 | 
Companies | 10? | 100s?
Incentive | Improve technology & increase market share | Successful operation at handover of each customized plant
http://www.industry.siemens.com/Water/en/markets/p_02.htm

## Slide 30: Why has the Private Sector Failed to Optimize Municipal Water Treatment?
Research and development is expensive
Low volume of units and customized designs for each site
Long life of units
Vendors want to sell hardware
Consultants want to minimize liability for design
Consultants use vendors to create their designs
Vendor designs are patented to maintain market
Can’t risk failure on a unit – conservative design prevails
Ineffective feedback mechanism
Notes: R&D is expensive

## Slide 31: Package Plants

## Slide 32
Dominant Design Constraint?
Notes: What was the constraint used to create this design???? Constraints matter! The design you create will strongly reflect the constraints that you used to guide the design.

## Slide 34: Failure to design for the Operator

## Slide 35: Failure to design for the Operator

## Slide 36: Failure to design for the Operator

## Slide 38: Both “advanced” and “appropriate” technologies can fail
El Progreso,
  Modular BEKOX
  Vulnerable
Siguatepeque
  Civil Work
  Vulnerable
Marcala, Honduras
  No chemicals
  Upflow filtration
  Abandoned (Replaced with AguaClara)
4 veces mas cara que AguaClara
Notes: Ethics of Engineering Experimentation

## Slide 39: A Role for Universities
Develop new knowledge
Test the designs in full scale field trials
Make that knowledge available to the global community
Open source engineering!
Capacity building: training the trainers
Bring the power of automation to engineering design (Take Henry Ford’s idea out of the realm of widgets and into the realm of knowledge)

## Slide 40: Open-Source University-based Research and Development
Design Studio
Sustainable Infrastructure
New Theories
Research Laboratory
Safe water on tap
Journey Inward
Journey Outward
Notes: From the research lab to new understanding of the physics to the design studio to the construction site to the tap
"research invent design empower"

## Slide 41: Low Carbon Footprint Technologies
Previous generations of engineers designed infrastructure that required cheap fossil fuel
It is long past time for a new paradigm
The original motivation for developing energy efficient technologies was the Global South, but many of these technologies will be the preferred option for wealthier communities too (Everyone likes cheaper, better, more reliable)

## Slide 42: Hypotheses: The Grand Experiment
Technology should be designed based on the conditions under which it will operate
For infrastructure it is more efficient to disseminate knowledge than hardware
We can achieve higher coverage using a model of technology dissemination in which we share knowledge openly

## Slide 43: Where are we going?
Control and measure flow
Rapid Mix
Flocculation
Sedimentation
Disinfection
Filtration
The Challenge!